## Slide 1: Contrail DPDK VROUTERS INTERNAL DETAILS
Laurent DURAND
Version 1.0 – March 2020

## Slide 2
MULTI Q VNFs
SINGLE Q VNFs
VIF COUNTERS
VROUTER FINE TUNING PARAMETERS

## Slide 3: vRouter packets processing summary
3 main parts are involved into vRouter DPDK packet processing:
Physical NIC and its “DPDK queues” (aka rings)
vrouter lcores (aka DPDK forwarding threads)
VNF virtual NICs and its “queues” (aka VirtIO rings)
vRouter packet forwarding is performed in two steps :
First step : packet polling. A lcore is extracting an incoming packet from a queue of a source interface
Second step : packet processing. A lcore (same or distinct from polling one) is processing the packet and push it in a queue of destination interface.
In between polling lcores and processing lcores there are some “buffers” aka vrouter queues

## Slide 4
MULTIQ VNFs

## Slide 5: UPSTREAM TRAFFIC (MPLSoUDP or VXLAN)
Incoming encapsulated packets are well balanced onto vif0 (DPDK interface for physical NIC) queues thanks to UDP good entropy.
DPDK RSS hash is spreading all incoming packets on vif0 RX queues. As the incoming traffic is well spread on all queues, there is no need to rebalance it among the processing core. The polling cores are processing cores are the same. vRouter internal queues are unused in this particular case.
Once the incoming packet has been processed, the processing core is writing the packet into the virtio ring of the destination virtual interface attached to it.
It will be up to the virtual instance DPDK application to poll the packet from the VirtIO ring to get it processed into the VM. And so to free the space used by this packet into the VIF queue.
With MPLS over UDP we have a good traffic balancing onto the vrouter core and also onto the vif queues.

## Slide 6: UPSTREAM TRAFFIC (MPLSoGRE)
Incoming encapsulated packets are unequally balanced onto vif0 (DPDK interface for physical NIC) queues. In most of the case all the traffic is sent to a single queues (due to RSS hash calculation is always giving the same result). The other queues are remaining unused (empty) to the bad traffic balancing.
This is why when GRE is used, an additional hash is calculation is made into the vrouter onto the decapsulated packet (MPLSoGRE inner packet). This hash calculation is used to select a processing cores among the other lcores. The polled packet is then put into the vrouter internal queue bound to processing core. The processing core will extract all incoming packets into its processing queue and will calculate the destination vif.
Once the incoming packet has been processed, the processing core is writing the packet into the virtio ring of the destination virtual interface attached to it.
It will be up to the virtual instance DPDK application to poll the packet from the VirtIO ring to get it processed into the VM. And so to free the space used by this packet into the VIF queue.
With MPLS over GRE we do not have a good traffic balancing onto the vrouter core. This is why incoming packets are rebalanced internally. It improves the workload spread onto lcores, but the queues are not equally load balanced.

## Slide 7: DOWNSTREAM TRAFFIC
Incoming packets are balanced onto the VNF vif according to VNF DPDK application. Traffic could be or not equally balanced on all vif queues.
This is why, for downstream traffic, an additional hash is calculation is made into the vrouter in order to balance VNF traffic among the lcores. This hash calculation is used to select a processing cores among other lcores than those used for polling a given queue. The polled packet is then put into the vrouter internal queue bound to each processing core. The processing core is extracting all incoming packets into its processing queue and is calculating the destination vif (in our case it will be vif 0/0).
Once the incoming packet has been processed, the processing core is writing the packet into the queue of the physical interface attached to it.
It will be up to the virtual instance DPDK application to poll the packet from the VirtIO ring to get it processed into the VM. And so to free the space used by this packet into the VIF queue.
Additional hash calculation done in the vrouter leads to a good traffic spreading among lcores but is very costly and has a bad impact on performances.

## Slide 8
SINGLEQ VNFs

## Slide 9: UPSTREAM TRAFFIC (MPLSoUDP or VXLAN)
Incoming encapsulated packets are well balanced onto vif0 (DPDK interface for physical NIC) queues thanks to UDP good entropy.
DPDK RSS hash is spreading all incoming packets on vif0 RX queues. As the incoming traffic is well spread on all queues, there is no need to rebalance it among the processing core. The polling cores are processing cores are the same. vRouter internal queues are unused in this particular case.
Once the incoming packet has been processed, the processing core is writing the packet into the unique virtio ring.
It will be up to the virtual instance DPDK application to poll the packet from the VirtIO ring to get it processed into the VM And so to free the space used by this packet into the VIF queue.
With single Q VNF, all processing cores are in a “race condition” to write into the single queue presented by the vif:
When there is a lot of processing cores (more than 4) it can lead to jitter and even to packet drops (it creates burst into packet delivery into the queue).

## Slide 10: UPSTREAM TRAFFIC (MPLSoGRE)
Incoming encapsulated packets are unequally balanced onto vif0 (DPDK interface for physical NIC) queues. In most of the case all the traffic is sent to a single queues (due to RSS hash calculation is always giving the same result). The other queues are remaining unused (empty) to the bad traffic balancing.
This is why when GRE is used, an additional hash is calculation is made into the vrouter onto the decapsulated packet (MPLSoGRE inner packet). This hash calculation is used to select a processing cores among the other lcores. The polled packet is then put into the vrouter internal queue bound to processing core. The processing core will extract all incoming packets into its processing queue and will calculate the destination vif.
Once the incoming packet has been processed, the processing core is writing the packet into the unique virtio ring of the destination vif.
It will be up to the virtual instance DPDK application to poll the packet from the VirtIO ring to get it processed into the VM. And so to free the space used by this packet into the VIF queue.
With single Q VNF, all processing cores are in a “race condition” to write into the single queue presented by the vif:
When there is a lot of processing cores (more than 4) it can lead to jitter and even to packet drops (it creates burst into packet delivery into the queue).

## Slide 11: DOWNSTREAM TRAFFIC
Incoming packets are sent into the single vif queue. Only one lcore is selected to poll this queue.
This is why, an additional hash is calculation is made into the vrouter in order to balance VNF traffic among the lcores. This hash calculation is used to select a processing cores among other lcores than those used for polling a given queue. The polled packet is then put into the vrouter internal queue bound to each processing core. The processing core is extracting all incoming packets into its processing queue and is calculating the destination vif (in our case it will be vif 0/0).
Once the incoming packet has been processed, the processing core is writing the packet into the queue of the physical interface attached to it.
It will be up to the virtual instance DPDK application to poll the packet from the VirtIO ring to get it processed into the VM. And so to free the space used by this packet into the VIF queue.
Additional hash calculation done in the vrouter leads to a good traffic spreading among lcores but is very costly and has a bad impact on performances.

## Slide 12
VIF COUNTERS

## Slide 13: UPSTREAM COUNTERS
Incoming flows from underlay network destinated to a VM interface:

## Slide 14: DOWNSTREAM COUNTERS
Incoming flows from a VM interface destinated to underlay network:

## Slide 15: UNDERLAY TO VM (MPLSoUDP) – 1 FLOW
We have generated a single UDP flow stream (no entropy). All the traffic is processed by the same core.
All counters have the same values (difference is due to observation delays)

## Slide 16: VM to Underlay – 1 flow
We have generated a single UDP flow stream (no entropy). Core 13 is the polling core. Internal vrouter hashing algorithm has selected core 11 as processing core.

## Slide 17: UNDERLAY TO VM (MPLSoUDP) – 2 FLOWs
We have generated a two UDP flows stream. The incoming traffic is processed by two distinct cores.

## Slide 18: VM TO underlay – 2 FLOWS
We have generated a two UDP flows stream. The incoming traffic is processed by two distinct cores.
Core 11 and Core 13 are the polling cores. The hashing algorithm has reselected the same core, but each flow is processed by the other core :

## Slide 19: UNDERLAY TO VM (MPLSoUDP) – 4 FLOWs
We have generated a 4 UDP flows stream. Due to the poor entropy, the hash (calculated on physical NIC) algorithm has spread them on only 3 cores. 2 UDP flows are processed by core 14.
PS: Part of the traffic has been lost before to reach this compute (800 KPPS instead of 1200 KPPS).

## Slide 20: VM TO underlay – 4 FLOWS
We have generated a four UDP flows stream. The incoming traffic is processed by 3 distinct cores as these flows are sent on only 3 queues by the VM (poor entropy give some redundant hash results).
vRouter hashing algorithm used to select the polling core is splitting the “fat flows’ into two distinct flows. 4 processing cores are involved :

## Slide 21: vRouter INTERNAL DROP
Here we have generated a single UDP flow stream. The generator is sending this flow onto 2 different queues. 2 polling core are involved onto the vrouter. vRouter hashing algorithm is selecting same core (core 14) to process this single UDP flow.
We can notice that lots of RX Queue errors are occurring.

## Slide 22: vRouter INTERNAL DROP
Here we have the details of internal drops that are done inside the vrouter due to a lack of capacity of the processing core.
Processing core is generating all the drops. 87% of dropped packets are coming from core 11 and 13% are coming from core 12.

## Slide 23: Key Take AWAY
A poor entropy is generating lots of side effects and has a big impact on vrouter performance.
Some interesting counters to check:
TX Port errors: VM is too slow to pick-up packets
RX queue errors: forwarding cores was not fast enough to process incoming packets
How to read RX queue errors counter ?
  vif --get <interface> --core <forwarding core> : is returning drop statistics generated onto a given forwarding core.
$ vif --get 3 --core 11 | grep "RX queue errors"
RX queue errors to lcore 0 0 0 0 0 0 0 0 0 0 27283689 0 7534963 9294274 6851459 5748667
xxx: forwarding core which drop packets
xxx: polling core whose packets have been drop

## Slide 24: Key Take AWAY
When drops are occurring inside the vrouter, it can be checked into “RX queue errors” counter or “IF Drop” in drop statistic option.
$ vif --get 3 --get-drop-stats | grep "IF Drop“
IF Drop 325686650
$ vif --get 3 | grep "RX queue packets“
RX queue packets:73891601519 errors:325686650
This value also matches RX Ports packets – RX Packets value:
$ vif --get 3 | grep "RX packets"
RX packets:73891746924 bytes:4433501752754 errors:0
$ vif --get 3 | grep "RX port"
RX port packets:74217433574 errors:0 syscalls:1
PS: dpdkvifstats.py tools is providing statistics for RX and TX packets counters (forwarding cores statistics).

## Slide 25
VROUTER FINE TUNING PARAMETERS

## Slide 26: Vrouter fine tuning parameters
vrouter fine tuning parameters are foreseen for future version and should give more options to get more performance.
/!\: Not all new parameters are committed yet.
vrouter fine tuning will remain a trade-off between :
throughput
jitter/delay
traffic flows balancing on DPDK cores
CPU allocation
Enable or not some options will have to be done according the expected traffic flow matrix and performance

## Slide 27: What about VIF queue size ?
Rqueue Size are defined at OpenStack level (using libvirt) : /etc/nova/nova.conf
# Configure virtio rx queue size.
#
# This option is only usable for virtio-net device with vhost and
# vhost-user backend. Available only with QEMU/KVM. Requires libvirt
# v2.3 QEMU v2.7. (integer value)
# Possible values:
# 256 - <No description provided>
# 512 - <No description provided>
# 1024 - <No description provided>
#rx_queue_size=<None>
# Configure virtio tx queue size.
#
# This option is only usable for virtio-net device with vhost-user
# backend. Available only with QEMU/KVM. Requires libvirt v3.7 QEMU
# v2.10. (integer value)
# Possible values:
# 256 - <No description provided>
# 512 - <No description provided>
# 1024 - <No description provided>
#tx_queue_size=<None>

## Slide 28: What about VIF queue size ?
It can be configured with TripleO (puppet/services/nova-compute.yaml) :
NovaLibvirtRxQueueSize:
description: >
virtio-net RX queue size. Valid values are 256, 512, 1024
default: 512
type: number
constraints:
- allowed_values: [ 256, 512, 1024 ]
tags:
- role_specific
NovaLibvirtTxQueueSize:
description: >
virtio-net TX queue size. Valid values are 256, 512, 1024
default: 512
type: number
constraints:
- allowed_values: [ 256, 512, 1024 ]